## Slide 1: PEREGRINE
DISASTER-RESILIENT BROADCAST NETWORK
A broadcast-resilience planning and alert hub that estimates how warning reach changes during cascading infrastructure failures, and compares recovery interventions under explicit, inspectable assumptions.
SIMULATION
FICTIONAL / ASSUMED DATA
IEEE BTS HACKATHON · SOURCE OF TRUTH v2.1 (DRAFT) · 10 OCT 2026
RESILIENCE_S30
MODEL OUTPUT
78.07%
Healthy network · cell-only
30-MINUTE ALERT WINDOW
Notes: Open on the SIMULATION label and the fictional-data notice. Everything on screen is computed from documented assumptions; none of it is field data. No tagline is shown because the team has not yet resolved the tagline conflict (Q19). The gauge shows the reproduced healthy, cell-only S30 value of 78.07% (test vector T-S30-01).

## Slide 2: Backup channels can share one dependency
01 · PROBLEM
Three channels on paper are not three independent paths
DERIVED · KARAI, UPPALAM, SAGAR · ONE EAST POWER CUT
power_east
CUT
gateway
up
Cell broadcast
needs power_east
DOWN
FM broadcast
needs power_east
DOWN
Shelter mesh
needs gateway
AVAILABLE
Tower B villages: 1 channel left (mesh, if a node is present)
01
Disasters fail together
Power, fibre, towers, transmitters and gateways fail in correlated ways.
02
Channels look redundant
Several warning channels can quietly share one critical dependency.
03
Planners need answers
How much warning reach survives over time, which weakness matters most, and which intervention restores the most.
NORTH STAR
Help emergency broadcasters understand how warnings degrade when infrastructure fails, identify the most consequential weaknesses, and compare recovery interventions using explicit, inspectable assumptions.
Notes: The core pain point: disasters cause correlated failures, so channels that look redundant may share a hidden dependency. The diagram is derived by hand from the documented dependency table (Section 6.2): cell broadcast and FM in the Tower B villages both depend on power_east. It is illustrative, not a field finding. The shelter mesh is shown as surviving only if the village has a mesh node, which is still UNVERIFIED in the bible (Q11).

## Slide 3: A planning simulation, not an alert system
02 · POSITIONING
Decision support for the broadcast network that carries warnings
PEREGRINE IS
A decision-support simulation for emergency broadcasting resilience
A way to see how warning reach degrades across cascading failures
Complementary to SACHET, broadcasters and operators, not a replacement
PEREGRINE IS NOT
A generic mesh-chat app or disaster dashboard
An authority that issues real emergency alerts
A deployed system, or one validated with field data
An AI product by default: transparent models come first
INTENDED USER GROUPS · NOT CONFIRMED CUSTOMERS OR PARTNERS
U1
Emergency broadcasters and broadcast-network planners
U2
Disaster-management authorities and resilience planners
U3
Infrastructure operators weighing backup power or alternate gateways
U4
Researchers and educators in disaster communication
Notes: Be explicit about scope. PEREGRINE is a planning simulation and alert-hub concept; it does not replace SACHET, broadcasters or telecom operators. The user groups are intended audiences, not confirmed customers or partners. Do not claim the project is deployed, field-tested or integrated with any operator.

## Slide 4: A dependency graph links failures to reach
03 · SYSTEM MODEL
Each channel is available only if every upstream node is up
power_west
fibre
power_east
gateway
Cell broadcast · Tower A
needs fibre · tower_A · power_west
Kovalam, Pazhaya, Marina · 11,200
Cell broadcast · Tower B
needs fibre · tower_B · power_east
Karai, Uppalam, Sagar · 7,200
FM broadcast
needs fm_tx · power_east
Six tower-covered villages · 18,400
Shelter mesh
needs gateway · own mesh node
Six villages with a node (which six: UNVERIFIED)
8
fictional villages
19,900
modelled people
7
failure toggles + cyclone preset
Thoni and Hill Camp: 1,500 people with no tower and no FM coverage
Notes: Eight fictional villages, 19,900 people, two cell towers. Channel upstream sets come from Section 6.2 and are marked [ASSUMPTION - confirm in code]. Tower A serves 11,200 people, Tower B 7,200, and 1,500 people (Thoni and Hill Camp) have neither tower nor FM. Which six villages have a shelter mesh node, and the map coordinates, are still unverified and must be read from the prototype code.

## Slide 5: Two scenarios, never on one axis
04 · SCENARIOS
Different time models: results from S30 and S72 are not comparable
S30
Alert window
WINDOW
30 minutes
TIME MODEL
Arrival time. A person reached at time a contributes (window − a) / window
CHANNELS
Cell broadcast, FM and shelter mesh, per failure toggles
18,400 × 0.85 × (30 − 0.2) / 30
÷ 19,900 = 78.07%
REPRODUCED · HEALTHY, CELL-ONLY
S72
Outage plan
WINDOW
72 hours
TIME MODEL
Availability. The fraction of the 72 hours a service is on air
ASSUMPTIONS
Only FM can be on air. Power fails at hour 0, grid returns at hour 48, generator runs 25 h, mobile unit arrives at hour 24
reach_FM = 0.55 × (a + (1 − a) × 0.25)
overall = reach_FM × 18,400/19,900 × h/72
REPRODUCED · ALL 12 MATRIX CELLS
≠
Notes: S30 uses an arrival-time model over 30 minutes. S72 uses an availability model over 72 hours. They must never be mixed on one axis. The formulas in the dark chambers are re-derived by hand from the documented assumptions (Section 6.6); they confirm the documentation is self-consistent, not that the running code matches. Acceptance tests T-S30-01 and T-S72-01 check the code against these values.

## Slide 6: Cell-only reach falls to zero in the cyclone
05 · S30 RESULTS
Other modelled channels keep some reach when the cell channel is lost
Chart: Resilience score, S30 (%)
| Cell-only | All channels | All + response plan
Healthy network | 78 | 87 | 89
Cyclone preset | 0 | 54 | 56
S30 · 30-MINUTE ALERT WINDOW · SIMULATION OUTPUT, NOT A PREDICTION
Cell-only
HEALTHY → CYCLONE
78 → 0
All channels
HEALTHY → CYCLONE
87 → 54
All + response plan
HEALTHY → CYCLONE
89 → 56
KNOWN WEAKNESS
The cyclone preset keeps the gateway alive, hiding a single point of failure. Gateway loss is tested separately.
Notes: Reported S30 defaults: healthy 78 / 87 / 89 percent for cell-only / all channels / all channels plus response plan; cyclone preset 0 / 54 / 56. These are simulation outputs under illustrative assumptions, not predictions. Be upfront about the known weakness: the cyclone preset keeps the gateway alive. The team decided to fix this; gateway loss must be an explicit, separately testable demo beat (Q17).

## Slide 7: Fibre is the costliest single failure
06 · FAILURE DIAGNOSIS
Ranked by resilience lost when one component fails
Chart: Resilience lost when one component fails (percentage points)
| Fibre cut | West power cut | Tower A collapse | East power cut | Tower B collapse | Gateway lost | FM fault
Resilience lost (points) | 27.9 | 17 | 17 | 13.3 | 11 | 7 | 0.7
MODEL OUTPUTS UNDER ASSUMPTIONS · NOT PREDICTIONS
HOW TO READ IT
Both towers need fibre for cell broadcast, so one fibre cut removes the cell channel everywhere. Power and tower failures hit one tower group at a time.
CAUTION
The 54-point drop at the gateway step of the worst-first sequence depends on failure order. We test several orders and never present it as a fixed real-world impact.
Notes: Single-failure impacts reported by the prototype: fibre 27.9, west power 17.0, Tower A 17.0, east power 13.3, Tower B 11.0, gateway 7.0, FM fault 0.7 percentage points. Fibre ranks first because, by the documented dependency table, both towers need it for cell broadcast. These are simulation outputs under assumptions, not predictions. The sequence view depends on failure order (Section 6.7).

## Slide 8: Generators plus a mobile unit triple reach
07 · 72-HOUR OUTAGE PLAN
Time-averaged expected reception over 72 hours, population-weighted
PLAN | ON AIR (HOURS) | AUTO: NONE | AUTO: HALF | AUTO: ALL
No investment | 48–72 (24 h) | 4.2% | 10.6% | 17.0%
Backup generators | 0–25 · 48–72 (49 h) | 8.7% | 21.6% | 34.6%
Mobile broadcast unit | 24–72 (48 h) | 8.5% | 21.2% | 33.9%
Generator + mobile unit | 0–72 (72 h) | 12.7% | 31.8% | 50.9%
S72 · REPRODUCED FROM THE DOCUMENTED FORMULA · SIMULATION OUTPUT
This is time-averaged expected reception, not “population reached”. Auto-tune is a scenario variable, not a statement about real phones or radios.
READ THE SPREAD
Adding both interventions lifts every column threefold: 4.2% to 12.7%, and 17.0% to 50.9% at full auto-tune.
DERIVED
Thoni and Hill Camp get nothing in any plan. They have no tower and no FM, so generators and the mobile unit cannot reach them.
Notes: Every cell in this matrix was re-derived by hand from the documented formula: reach_FM(a) = 0.55 x (a + (1 - a) x 0.25), times 18,400 / 19,900, times hours-on-air / 72. All twelve cells round to the prototype values (4/11/17, 9/22/35, 8/21/34, 13/32/51). Call it time-averaged expected reception, not population reached. The Thoni and Hill Camp finding is derived by hand and must be confirmed in code; it is the model-based reason the fairness story needs a village-specific intervention.

## Slide 9: Silence Clock: hours with no warning path
08 · SILENCE CLOCK
Modelled hours per village across the 72-hour outage
PROPOSED · NOT YET BUILT
No investment
ON AIR 48–72 H
FM VILLAGES (SIX)
4
8
H
BASELINE
THONI · HILL CAMP
7
2
H
NO MODELLED PATH
Backup generators
ON AIR 0–25 · 48–72 H
FM VILLAGES (SIX)
2
3
H
−25 H VS NO INVESTMENT
THONI · HILL CAMP
7
2
H
NO MODELLED PATH
Mobile broadcast unit
ON AIR 24–72 H
FM VILLAGES (SIX)
2
4
H
−24 H VS NO INVESTMENT
THONI · HILL CAMP
7
2
H
NO MODELLED PATH
Generator + mobile unit
ON AIR 0–72 H
FM VILLAGES (SIX)
0
H
−48 H VS NO INVESTMENT
THONI · HILL CAMP
7
2
H
NO MODELLED PATH
SilenceHours = Σ (1 − PathAvailable(t)) · Δt. Computed from the per-village series only: modelled hours with no available path, not proof that nobody heard a warning.
Notes: PROPOSED, not yet built. Values are derived by hand from the same on-air windows as the S72 matrix: the six tower-covered (FM) villages are silent for 48 h with no investment, 23 h with generators, 24 h with the mobile unit and 0 h with both. Thoni and Hill Camp are silent for all 72 hours in every plan. Acceptance tests T-SIL-01 and T-SIL-02 must pass before this is described as implemented. Always call it modelled hours with no available warning path.

## Slide 10: Redundancy Illusion: count channels honestly
09 · REDUNDANCY ILLUSION
Nominal channels versus what survives one more failure
PROPOSED · NOT YET BUILT
DERIVED · HEALTHY NETWORK · COMMON-CAUSE NODE OUTLINED
power_east
common-cause node
gateway
up
Cell broadcast
needs power_east
AVAILABLE
FM broadcast
needs power_east
AVAILABLE
Shelter mesh
needs gateway
AVAILABLE
Tower B villages: Karai · Uppalam · Sagar
No single node is shared by all three channels. The illusion shows up where cell and FM share power_east, and after compound failures when mesh via the gateway is the last path.
KARAI · HEALTHY
DERIVED
3
on paper
3
available now
1
after one more failure
MARINA · HEALTHY
DERIVED
3
on paper
3
available now
2
after one more failure
ASSUMES A MESH NODE · CONFIRM IN CODE
Notes: PROPOSED, not yet built. We corrected our own planning note: by the documented dependencies there is no single node shared by all three channels for any village. The illusion appears in two documented forms. First, in Tower B villages (Karai, Uppalam, Sagar) cell broadcast and FM both depend on power_east, so one east power cut removes both and only the mesh remains. Second, after compound failures such as the cyclone preset, the mesh via the gateway can be the last path. By hand: Karai is 3 on paper, 3 available, 1 guaranteed after one more failure; Marina is 3, 3 and 2. Never force a dramatic 3-to-0 transition; show whatever the graph computes. Confirm against code (T-ILL-02, T-ILL-03).

## Slide 11: Save the most, or leave no one behind
10 · DECISION ENGINE
One budget, one scenario, two objectives, compared on identical inputs
PROPOSED · NOT YET BUILT
A
Reach maximiser
SAVE THE MOST PEOPLE
Maximises overall reach within the budget.
Risk: a large village can outweigh a small one.
B
Fairness-constrained
LEAVE NO ONE BEHIND
Requires every village to reach a minimum first, then maximises the rest.
Trade-off: may cost more or lower the best average.
01
Simulate the baseline
02
Score gain per cost
03
Apply the best, repeat
04
Re-simulate from scratch
GREEDY HEURISTIC · NOT GUARANTEED OPTIMAL · FLOOR MISSED IS REPORTED, NEVER HIDDEN
DECISION NEEDED
Generators and the mobile unit cannot reach Thoni or Hill Camp. Recommended: run the fairness comparison on S30, where relay nodes and sirens target unreached villages.
Notes: PROPOSED, not yet built. If the planner is not built and tested, do not call the current matrix an optimiser. The planner is a greedy, simulation-in-the-loop heuristic: it scores each candidate by gain per cost, applies the best, and re-simulates from scratch at the end. It does not guarantee a global optimum; with about 12 candidates the team can enumerate every subset to report the optimality gap honestly. The central insight, that the best plan on average may leave the smallest village worst off, is a testable hypothesis, not a given. Decision Q13 is open: option 1 runs the fairness comparison on S30. Costs are placeholder budget units until defensible figures exist (Q9).

## Slide 12: Signed alerts, verified in the browser
11 · INTEGRITY
The label reflects a real signature check, not a green badge
IMPLEMENTED · VERIFY BUILD
01
Sign
ECDSA P-256 signature created in the browser
SIGNED
02
Verify
Status comes from actually verifying the signature
VERIFIED
03
Tamper test
Changing a signed message must show it rejected
REJECTED
04
Withdraw
A separate signed event tied to the original alert ID
WITHDRAWN
LIMITS: STATE THEM IF ASKED
Signed alerts alone do not eliminate misinformation or prove issuer authority. That needs trust keys, issuance authority and verification procedures.
SIMULATED ALERTS ONLY
No real location-specific warnings. CAP-style fields are an interoperability direction, not a claim of certified CAP conformance.
Notes: Reported as implemented in the prototype but the tested status is still open (Q8): smoke-test sign, verify, tamper and withdraw on the presenting machine before demoing. Keep the integrity demo to about 15 seconds. The stamps name the UI states; they are labels, and the underlying state must be true. A withdrawal is a separate authenticated event, not an edit of the original alert.

## Slide 13: What is built, proposed and out of scope
12 · PROJECT STATUS
Implemented, assumed and planned stay visibly separate
IMPLEMENTED · VERIFY BUILD
8 fictional villages, 19,900 people
Failure toggles and cyclone preset
S30 score and 3-way comparison
Failure-impact ranking
72-hour outage-plan matrix
Alert composer with channel payloads
ECDSA signing, tamper demo, withdrawal
SMOKE-TEST EVERY CONTROL BEFORE DEMO DAY.
PROPOSED · PRIORITY ORDER
P0 Audit and stabilise the model
P1 Silence Clock
P2 Budget planner, two objectives
P3 Redundancy Illusion panel
P4 Baselines and experiment log
P5 Sensitivity panel
P6 Last-mile view, one village
AUDIT FIRST: EVERY METRIC INHERITS ANY BUG.
OUT OF SCOPE · 6-HOUR BUILD
Real emergency alert distribution
SACHET or operator integration claims
Phone auto-wake support claims
Deployable radio or LoRa transmission
Real-world effectiveness claims from simulation
Notes: A clear status picture builds trust with judges. Left: reported as implemented in the prototype (verify in the running build). Middle: proposed work in priority order; none of it may be presented as implemented in UI text, slides or demo scripts. Right: explicitly out of scope for a six-hour, software-only build.

## Slide 14: What the simulation does and does not prove
13 · LIMITATIONS
Evidence level decides the words we are allowed to use
Simulation demonstration
“The model shows…”
WE ARE HERE
Event-grounded simulation
“Under assumptions grounded in…”
Expert review
“Reviewed by…” (only if true)
Field validation
Only if it happened
SAFE TO SAY
The model shows how dependency assumptions change warning resilience
Channels and outage plans are compared under explicit assumptions
Existing alert systems are complementary, not replaced
DO NOT CLAIM
Scores describe actual reach in a real disaster
Field-tested, deployed, or integrated with SACHET
First, unique or optimal: the greedy planner is a heuristic
Silence hours prove nobody heard a warning
Notes: The bible asks the team to add a limitations slide themselves. Never say field-tested, proven in disasters, or validated in the real world. Do not say first, only or unique without a documented prior-art review. If asked about the numbers: the village world and most channel values are assumptions chosen for an interactive simulation; the result shows what follows from those assumptions, not a prediction of a real disaster.

## Slide 15: Next: validate on real network data
From a transparent simulation to evidence
01
Audit the model against the reproduced test vectors
02
Build the Silence Clock, planner and Redundancy Illusion panel
03
Compare against baselines A to D and test ±30% assumption changes
04
Validate against real network and receiver data
WHAT WE ARE SAYING
The current prototype is a transparent simulation. Its inputs are illustrative, and the next step is to test its recommendations against simple baselines and check how robust they are to uncertainty.
PEREGRINE
DISASTER-RESILIENT BROADCAST NETWORK
Notes: Close on the honest framing: a transparent simulation with illustrative inputs. The next research step is to compare the planner against simple baselines (cell-only, independence-assuming estimator, diagnosis without optimisation) and test how robust conclusions are to a plus or minus 30 percent change in assumptions. Open decisions to settle before the final pitch: fairness scenario (Q13), cyclone preset gateway behaviour (Q17), tagline (Q19) and the master brand asset (Q20). The falcon symbol is intentionally absent: the master vector does not exist yet and the brand rules say not to redraw it.